## Slide 1
CAPTIA-CONNECT
Partner Integration Guide
Bring your devices, sensors and gateways onto our IoT edge platform
MQTT-native
Multi-tenant
Edge-resilient
v1.0 · 2026-05 · partners@captiatechnology.com
Confidential — for partner evaluation

## Slide 2
01 · OVERVIEW
What CAPTIA-connect is
2 / 14
CAPTIA Technology · Partner Integration Guide
CAPTIA-connect is the on-premise IoT runtime deployed at every customer site. It ingests device telemetry over MQTT, persists it in InfluxDB with tiered retention, exposes a REST/SSE API for dashboards, and runs an event-rules engine — all packaged as a Docker Compose stack on bare-metal Ubuntu 24.04.
Ingest
MQTT 7-segment topics with JSON payloads. Telegraf does dual-stream routing: raw to telemetry, deduped on-change to state_events.
Persist
InfluxDB 2.7 with 9 buckets (raw + 1m/15m/1h rollups + on-change + metadata). Cardinality-tuned schema, 14-day raw retention.
Process
Events Engine evaluates rules in real time with Redis-backed gate state. Normalizer translates vendor protocols into canonical CAPTIA topics.
Serve
Dashboard Adapter (FastAPI) exposes /v1/query, SSE streams, command bridge. Grafana, custom React UIs and the SaaS plane consume it.
29
containerized services
2
production tenants
<5s
MQTT-to-storage latency
365d
long-term retention (1h rollup)

## Slide 3
02 · ARCHITECTURE
End-to-end data flow
3 / 14
CAPTIA Technology · Partner Integration Guide
Your devices publish to the local Mosquitto broker. Telegraf and the Normalizer route data into InfluxDB. The Dashboard Adapter and the Events Engine read from there. Apps query the Adapter only — never InfluxDB directly.
Partner
Device
Native or vendor proto
Mosquitto
MQTT 1883/8883
Normalizer
+ Telegraf
Tag extraction · dedup
InfluxDB
telemetry · rollups
Adapter
+ Events
API · SSE · rules
Dashboards
+ SaaS
Grafana · React · BFF
WHERE PARTNERS PLUG IN
Stages 1–2: you publish to MQTT. Stages 3–6 are managed by CAPTIA — no work on your side.
WHAT CROSSES THE WIRE
Only JSON over MQTT. No vendor SDKs to embed, no firewall changes beyond a single broker port.
OBSERVABILITY
Every hop is instrumented (Prometheus, Loki, OpenTelemetry). We trace your samples end-to-end during onboarding.

## Slide 4
03 · CHOOSE YOUR PATH
Two ways to integrate
4 / 14
CAPTIA Technology · Partner Integration Guide
Pick the path that matches your firmware. Path A is the fastest if you can shape the payload. Path B keeps your firmware unchanged and pushes the work into CAPTIA.
PATH A · RECOMMENDED
Native CAPTIA payload
Your device publishes directly to canonical CAPTIA topics with the standard payload. Skips the normalizer.
Lowest latency (1 hop instead of 2)
No normalizer profile to author / maintain
Faster onboarding — typically days, not weeks
Best for new product lines or firmware in development
Effort: LOW
PATH B · DROP-IN
Vendor protocol → Normalizer
Your device speaks its native MQTT (or Modbus/OPC-UA via gateway). A YAML normalizer profile maps it to canonical topics.
Zero changes to your firmware
Profiles versioned in git, hot-reloaded at runtime
Per-device overrides for tagging exceptions
Suitable for fielded devices and OEM gateways
Effort: MEDIUM

## Slide 5
04 · CONTRACT
MQTT topic format (7 segments)
5 / 14
CAPTIA Technology · Partner Integration Guide
All telemetry rides on a strict 7-segment topic. Telegraf parses each segment into an indexed InfluxDB tag. Get this right and the rest is automatic.
captia
/
namespace
0
{env}
/
environment
1
{tenant}
/
domain_id
2
{site}
/
site_id
3
{device}
/
asset_id
4
telemetry
/
stream
5
{name}
variable
6
EXAMPLE — IES Simarro classroom
captia/prod/bms_classrooms/ies_simarro/AULA01/telemetry/co2
STREAM (segment 5) — five canonical values:
telemetry
Sensor readings / device state
cmd
Commands issued by adapter
ack
Device acknowledgment
state
Device state updates
event
Platform events (cmd_authorized, errors)

## Slide 6
05 · CONTRACT
MQTT payload schema
6 / 14
CAPTIA Technology · Partner Integration Guide
The payload is JSON. Telegraf forces fieldpass=["value"] — anything else is silently dropped. Multi-channel sensors must emit one MQTT message per channel with its own scalar value.
payload.json — telemetry stream
{
"value": 23.5,
"ts_ns": 1738749600000000000
}
// Optional fields — any other key is dropped:
// value → numeric (float) REQUIRED
// ts_ns → epoch nanoseconds RECOMMENDED
// (omit ts_ns → Telegraf uses its own clock)
Hard contract
Single field 'value' (float)
fieldpass = ["value"] in Telegraf
Optional 'ts_ns' for back-fill
Nanosecond epoch — preserves order
QoS 1 recommended
QoS 0 only for low-stakes signals
No multi-channel arrays
value_0_0…value_N_M are dropped
No nested objects
Flatten on device or via normalizer
No string values in 'value'
Use enum codes — declare in metadata
OTHER STREAMS — payload differs:
event → { ts, type, cmd_id, reason, error, ... } · cmd / ack → defined per device family

## Slide 7
06 · ROUTING
Continuous vs on-change signals
7 / 14
CAPTIA Technology · Partner Integration Guide
Telegraf classifies signals by the variable name (segment 7 of the topic). Continuous signals go to telemetry; on-change signals are deduped (heartbeat 168h) and routed to state_events. The naming convention IS the contract.
CONTINUOUS
Stored at every sample (5s)
Sensor readings: temperature, humidity, CO2, illuminance, occupancy ratio, sound level, IAQ, energy counters.
Goes to:
telemetry → rollups (1m / 15m / 1h)
metric_kind values:
analog_gauge · bool_presence · counter
ON-CHANGE
Stored only on transitions
Discrete signals: commands, acks, on/off states, setpoints, mode selectors, relay outputs, fault flags.
Goes to:
state_events (90d) + rollups
Variable suffix globs (auto-routed):
*_cmd *_ack *_status *_state *_st *_active
*_enable *_in_progress relay_* *_setpoint *_sp *_mode
Important: choose your variable names carefully — 'door_state' auto-routes on-change, 'door_position' does not. Mismatches cause data quality issues that are tedious to fix.

## Slide 8
07 · METADATA
Declare your variables in the catalog
8 / 14
CAPTIA Technology · Partner Integration Guide
Telegraf doesn't care about metadata, but the rest of the platform does. The InfluxDB bucket captia_metadata holds variable definitions that drive downsampling, dashboards, units and ranges. You declare each variable once, the platform routes the rest.
Required fields per variable
metric_kind
Drives downsampling
data_type
boolean / float / int / enum
unit
SI or textual (°C, %, ppm, lux…)
display_name
Localized label for dashboards
range_min/max
Validation + dashboard scaling
is_actuator
True if accepts /cmd/{name} writes
storage_mode
Derived from metric_kind
device_id
Maps to physical device record
metric_kind → storage → rollup stats
metric_kind | Storage | Stats produced
analog_gauge | continuous | mean / min / max
bool_presence | continuous | duty / count_rise / last
bool_state | on_change | last / count_rise
setpoint_step | on_change | last
counter | continuous | sum (delta)
skip | continuous | (no rollup)
Catalog is loaded by metadata-bootstrap on stack start, then editable via the Variable Config UI or our /v1/metadata/* API.
During onboarding we co-author the variables.yaml with you. You don't write JSON by hand.

## Slide 9
08 · NETWORK
How your devices reach the broker
9 / 14
CAPTIA Technology · Partner Integration Guide
Each CAPTIA edge server lives on the customer's OT LAN. Your devices reach the local Mosquitto broker over TCP. Anonymous access is enforced by network topology — there are no broker passwords by default.
Edge server — OT side
Sensor
Gateway
PLC / OPC-UA
Mosquitto
captia-mosquitto
:1883 / :8883 (TLS)
CAPTIA Pipeline
Telegraf · Normalizer · InfluxDB
Adapter API · Events Engine
Auth
Anonymous on the broker, segmented by network. mTLS available on :8883 if the partner requires it.
ACL
Per-tenant ACL is provisioned on the broker. We share device-specific topic patterns at onboarding.
VPN
Remote troubleshooting via Tailscale mesh. Partners get a guest user only for joint debugging windows.

## Slide 10
09 · PATH B DEEP-DIVE
Normalizer profile — the YAML DSL
10 / 14
CAPTIA Technology · Partner Integration Guide
If your firmware can't speak canonical CAPTIA, write a profile. The Normalizer is a microservice with hot-reload, fan-out, dedup and a DLQ. Profiles live in git, versioned and reviewed.
normalizer/profiles/<your-vendor>.yaml
id: sensup_v3
vendor: sensup
match:
topic: "sensup/sensor/+/data"
decode:
format: json
fan_out:
- source: $.tvoc
target_topic: "captia/{env}/{tenant}/{site}/{device}/telemetry/t-voc"
payload: { value: "$.tvoc", ts_ns: "$.timestamp_ns" }
- source: $.co2
target_topic: "captia/{env}/{tenant}/{site}/{device}/telemetry/co2"
device_overrides:
"0004742C0166": { asset_id: P1S01 }
Built-in features
Fan-out
One vendor message → N CAPTIA topics
Hot reload
Profile changes without restart
Dedup
Memory or Redis-backed, configurable
DLQ
Bad messages routed to MQTT DLQ topic
Per-device override
Tag exceptions without forking the profile
Pass-through
Topic-only rewrite (no payload reshape)

## Slide 11
10 · VALIDATION
Test your integration end-to-end
11 / 14
CAPTIA Technology · Partner Integration Guide
Every onboarding includes a sandbox tenant on a staging server. You can probe each layer with the tools below before we promote to production.
1 · Publish a test sample
mosquitto_pub -h <edge> -p 1883 \
-t "captia/dev/test/site01/device01/telemetry/temp" \
-m '{"value": 23.5}'
2 · Check arrival in InfluxDB
docker exec captia-influxdb influx query \
'from(bucket:"telemetry") |> range(start: -5m)
|> filter(fn: (r) => r.asset_id=="device01")'
3 · Visualize in Grafana
# Browse the built-in dashboard
https://<edge>:13000 → CAPTIA Live Telemetry
# Or query the adapter directly:
GET /v1/query?domain=...&site=...
4 · Health & readiness
curl http://<edge>:8100/healthz
curl http://<edge>:8100/readyz
curl http://<edge>:8090/healthz # normalizer
curl http://<edge>:8110/readyz # events

## Slide 12
11 · WORKFLOW
Onboarding in 5 steps
12 / 14
CAPTIA Technology · Partner Integration Guide
Typical timeline from kick-off to production: 4–6 weeks for Path A, 6–10 weeks for Path B, depending on the number of variables and protocol complexity.
01
Week 1
Discovery
Workshop: list devices, signals, ranges. Pick Path A or B.
02
Week 2
Spec
Co-author variables.yaml + topic map. Sign off the contract.
03
Week 3-4
Sandbox
Deploy on staging tenant. You publish, we observe.
04
Week 5
UAT
Joint validation, dashboard review, alarm rules tuning.
05
Week 6+
Production
Roll out to customer site under change control.

## Slide 13
12 · WHAT WE NEED FROM YOU
Partner deliverables
13 / 14
CAPTIA Technology · Partner Integration Guide
To kick off the discovery workshop in week 1 we ask for the following inputs. Anything missing pushes the timeline.
Device inventory
List of every device model, firmware version, serial-number scheme.
Signal catalog
All telemetry signals + units + valid ranges + sample rate.
Topic / payload spec
Path A: confirm canonical conformance. Path B: vendor topic + payload sample.
On-change vs continuous
Mark which signals are state/setpoint (on-change) vs sensor readings.
Auth requirements
If TLS or per-device certs are required, share the issuance plan.
Command surface
If you accept commands, list endpoints + payload contract + ack timing.
Test fleet
At least 1 device available for sandbox during UAT (week 3–5).
Support contact
One escalation owner for the integration window.
Send the checklist to partners@captiatechnology.com and we'll book the discovery workshop within 48h.

## Slide 14
14 / 14
READY TO INTEGRATE?
Let's build it together.
Partner desk
partners@captiatechnology.com
First reply within 1 business day
Engineering
integration@captiatechnology.com
Joint debug sessions during onboarding
Documentation
docs.captiatechnology.com
Topic ref, payload schema, OpenAPI
CAPTIA Technology · Partner Integration Guide · v1.0 · 2026-05